## Slide 1
PET solubility workflow with ORCA and openCOSMO-RS
From official openCOSMO-RS examples to PET-in-GVL/formic-acid calculations
Structure
PET trimer + solvents
>
ORCA
optimization + COSMORS SP
>
openCOSMO-RS
ln(gamma)
>
SLE
x and g/g solvent
Final numerical results: GVL = 0.334 g PET/g solvent (infinite dilution); formic acid = 4.59e-4 g PET/g solvent.
Files: pet_cosmors_hpc_package/pet_solubility_results.csv; generated by orca_full_workflow/08_calculate_pet_solubility.py

## Slide 2
What openCOSMO-RS_py contributes
Thermodynamic post-processing from COSMO surface information
openCOSMO-RS_py is a Python implementation of COSMO-RS with ORCA .orcacosmo parser support.
The working API is COSMORS(par=openCOSMORS24a()), add_molecule([...]), add_job(x, T, refst='pure_component'), calculate().
The model returns logarithmic activity coefficients ln(gamma); the solid solubility equation is a downstream thermodynamic calculation.
Official examples include activity coefficients, sigma-profile parsing, and paracetamol solubility.
Basis: openCOSMO-RS_py/README.md; openCOSMO-RS_py/examples/cosmors_calculation.ipynb cells 15, 27, 29

## Slide 3
OPI nightly documentation: role of ORCA
ORCA creates the quantum-chemical COSMO input files needed by openCOSMO-RS
OPI tutorial workflow: prepare structures, run ORCA with COSMORS keyword, parse .orcacosmo, then compute solubility.
Example ORCA setup uses calc.input.add_arbitrary_string('!COSMORS(ethanol)') and calc.input.ncores.
The tutorial explicitly checks normal ORCA termination before parsing the .orcacosmo output.
Our HPC implementation used direct ORCA input files instead of OPI, but kept the same COSMORS output target.
Basis: openCOSMO-RS - OPI nightly Docs.pdf, pp. 1, 2, 4, 5

## Slide 4
Official solubility equation in the tutorial
openCOSMO-RS gives ln(gamma); the SLE equation converts it to x
ln(x) + ln(gamma) = -DeltaHfus/R * (1/T - 1/Tfus)
Non-iterative: evaluate ln(gamma) at infinite dilution, x = exp(rhs - ln(gamma_inf)).
Iterative: solve ln(gamma(x)) + ln(x) - rhs = 0.
Reference state used in code: refst='pure_component'.
For literature-style screening, infinite-dilution values are the most directly comparable.
Basis: openCOSMO-RS - OPI nightly Docs.pdf, pp. 10-12; openCOSMO-RS_py/examples/cosmors_calculation.ipynb cell 29

## Slide 5
Lee et al. 2025: PET solubility screening context
The target paper uses COSMO-RS to screen dye/PET solubility across solvents
The article predicts PET and dye solubilities at 25 C and 100 C for 22 solvents.
GVL and acetic/formic acid family solvents appear in the solvent-screening context; acetic acid is highlighted experimentally.
The paper reports PET solubility in g solute per g solvent and uses the values to evaluate fibre preservation.
COSMO-RS is used as an equilibrium thermodynamic screen; kinetic and transport effects are outside the model.
Basis: Lee et al. 2025, Nature Sustainability, Fig. 1 and Methods, pp. 2-3, 8

## Slide 6
Lee et al. Methods: PET model and parameters
These are the parameters we mirrored in the PET calculation
Item | Lee et al. | Our calculation
PET model | PET trimer, ends capped with EG motifs | PET trimer from MD/optimized ORCA geometry
MD selection | 20 PET conformers from one 10 ns MD trajectory | 1 conformer used in this first test
Melting point | 260 C | 533.15 K
Fusion enthalpy | 54.3 J/g | converted to 34.674 kJ/mol using C32H30O14
Output unit | g/g solvent | mole fraction + g/g solvent
Basis: Lee et al. 2025 Methods, p. 8; our PET formula from pet_trimer_opt_final.xyz

## Slide 7
How our workflow maps to the literature workflow
Same concept, different quantum-chemistry implementation
Stage | Lee et al. | This work
Conformations | 20 PET conformers from MD | single PET trimer conformer
QM software | Gaussian 16 | ORCA 6.0.0 on HPC
COSMO-RS engine | COSMOtherm BP_TZVP_22 | openCOSMO-RS_py openCOSMORS24a
COSMO files | COSMO files for PET/solvents/dyes | .solute.orcacosmo for PET/GVL/formic acid
Solubility equation | chemical-potential based SLE | equivalent ln(gamma)-based SLE form
Basis: Lee et al. 2025 Methods, p. 8; openCOSMO-RS - OPI nightly Docs.pdf, pp. 10-12

## Slide 8
Local calculation files: geometry optimization
Three optimized species were used for the COSMORS single-point step
Species | Input/trajectory | ORCA opt level | Status
Formic acid | 31-CH2O2/31-CH2O2_opt_trj.xyz | M062X def2-TZVP D3zero Opt pal4 | converged
GVL | 34-C5H8O2/34-C5H8O2_opt_trj.xyz | M062X def2-TZVP D3zero Opt pal4 | converged
PET trimer | 35-PET/35-PET_opt_trj.xyz | M062X def2-SVP D3zero Opt pal64 | converged
Basis: 31-CH2O2/*_opt.out, 34-C5H8O2/*_opt.out, 35-PET/*_opt.out; files generated by 05/06 scripts

## Slide 9
Local calculation files: COSMORS single points
Final optimized structures were converted to .orcacosmo files
Species | ORCA input | Output used in openCOSMO-RS | Cores
PET trimer | pet_cosmors_hpc_package/pet_trimer.inp | pet_trimer.solute.orcacosmo | 64
GVL | pet_cosmors_hpc_package/gvl.inp | gvl.solute.orcacosmo | 4
Formic acid | pet_cosmors_hpc_package/formic_acid.inp | formic_acid.solute.orcacosmo | 4
ORCA line used: BLYP def2-SVP noautostart miniprint palN COSMORS(ethanol).
Only *.solute.orcacosmo files are used for PET-in-solvent calculations.
Basis: orca_full_workflow/07_prepare_pet_cosmors_package.py; pet_cosmors_hpc_package/*.inp

## Slide 10
Post-processing script
PET-specific wrapper around official openCOSMO-RS usage
Script: orca_full_workflow/08_calculate_pet_solubility.py
Reads PET, GVL and formic-acid .solute.orcacosmo files.
Uses openCOSMORS24a and refst='pure_component' to calculate ln(gamma).
Converts DeltaHfus = 54.3 J/g to J/mol using molar mass from PET XYZ.
Reports both mole fraction and g PET/g solvent.
Basis: orca_full_workflow/08_calculate_pet_solubility.py

## Slide 11
Unit conversion used for PET
Lee reports fusion enthalpy per gram; the SLE equation needs per mole
PET trimer formula: C32H30O14; M = 638.5722 g/mol
DeltaHfus = 54.3 J/g * 638.5722 g/mol = 34.674 kJ/mol
This conversion is required because the solid-liquid equilibrium equation uses molar thermodynamic quantities.
For polymer models, the molar mass must match the molecular representation used in the COSMO-RS calculation.
If a different PET oligomer length is used, the conversion must be updated.
Basis: Lee et al. 2025 Methods p. 8; pet_cosmors_hpc_package/pet_trimer_opt_final.xyz; 08_calculate_pet_solubility.py

## Slide 12
Final numerical results
Single-conformer PET trimer calculation at 298.15 K
Solvent | ln(gamma_inf) | x_inf | g/g_inf | x_iter | g/g_iter
GVL | -3.164 | 0.04973 | 0.3338 | 0.02943 | 0.1934
Formic acid | 4.152 | 3.307e-05 | 0.0004588 | 3.318e-05 | 0.0004603
Main interpretation: the calculated GVL value is much larger than formic acid. Using infinite-dilution g/g values, GVL is about 700x higher.
Basis: pet_cosmors_hpc_package/pet_solubility_results.csv

## Slide 13
Interpreting non-iterative vs iterative values
Which number should be used for comparison?
x_inf and g/g_inf use the infinite-dilution activity coefficient.
x_iter and g/g_iter solve the full composition-dependent equilibrium condition.
Lee et al. describe chemical potentials at infinite dilution in the solvent; for screening comparison, g/g_inf is the cleanest first comparison.
Iterative values are useful as a self-consistent correction when solubility is not extremely dilute.
Basis: openCOSMO-RS - OPI nightly Docs.pdf, pp. 8, 10-12; Lee et al. 2025 Methods p. 8

## Slide 14
Important caveats
Current result is a reproducibility test, not a full reproduction of Lee et al.
Only one PET conformation was used; Lee et al. used 20 PET trimer conformers from a 10 ns trajectory.
ORCA/openCOSMO-RS parameterization differs from Gaussian/COSMOtherm BP_TZVP_22 in the paper.
Our COSMORS single point used BLYP def2-SVP; higher basis or exact openCOSMO-RS recommended protocols may change values.
COSMO-RS predicts equilibrium thermodynamics; degradation, diffusion, swelling and fibre morphology are not captured.
Basis: Lee et al. 2025 Methods p. 8; Muller et al. 2025 openCOSMO-RS 24a discussion, p. 4

## Slide 15
Recommended next steps
How to move from first test to paper-level comparison
Extract multiple PET conformers from MD, preferably using the same selection criterion: lowest internal potential energy.
Run geometry optimization and COSMORS single-point calculations for each conformer.
Generate conformer-weighted or ensemble-averaged ln(gamma)/chemical-potential estimates.
Repeat for all target solvents and compare g/g_inf at 25 C and 100 C.
Document deviations from Lee et al.: software, parameterization, basis set, solvent conformer handling.
Basis: Lee et al. 2025 Methods p. 8; local scripts 06-08

## Slide 16
Appendix: local command sequence
Commands used in this reproduction
python orca_full_workflow/07_prepare_pet_cosmors_package.py
bash submit_all_cosmors.sh
bash check_cosmors_results.sh
python orca_full_workflow/08_calculate_pet_solubility.py --csv pet_cosmors_hpc_package/pet_solubility_results.csv
Inputs: pet_trimer.solute.orcacosmo, gvl.solute.orcacosmo, formic_acid.solute.orcacosmo
Basis: pet_cosmors_hpc_package/README_submit.md; orca_full_workflow/08_calculate_pet_solubility.py

## Slide 17
Appendix: source map
Where each claim in this deck comes from
Claim | Source
openCOSMO-RS API and examples | openCOSMO-RS_py README + examples/cosmors_calculation.ipynb
OPI/ORCA .orcacosmo workflow | openCOSMO-RS - OPI nightly Docs.pdf, pp. 1-5
Solubility formula and iterative/non-iterative methods | openCOSMO-RS - OPI nightly Docs.pdf, pp. 10-12
PET trimer, MD selection, 20 conformers | Lee et al. 2025 Methods, p. 8
PET Tm and DeltaHfus | Lee et al. 2025 Methods, p. 8
Our numerical results | pet_cosmors_hpc_package/pet_solubility_results.csv
Generated deck: PET_openCOSMO_RS_workflow_summary.pptx